ARTICLE XV

FLOODPLAIN OVERLAY DISTRICT (FP)

Section 1500	Purposes

The purpose of this Article is to:

A. 	Promote the general health, welfare, and safety of the community.

B. 	Encourage the utilization of appropriate construction practices in order to prevent or minimize flood damage in the future.

C. 	Minimize danger to public health by protecting water supply and natural drainage.

D. Reduce financial burdens imposed on the community, its governmental units, and its residents, by preventing excessive development in areas subject to flooding.

E. 	Comply with federal and state floodplain management requirements.

Section 1501	 Acronyms

The following acronyms are used throughout this Article:

A. 	ASCE – American Society of Civil Engineers

B. 	FEMA – Federal Emergency Management Agency

C. 	IBC – International Building Code

D. 	IRC – International Residential Code

E. 	UCC – Uniform Construction Code

Section 1502	 Issuance of Land Use Permit

A. 	The Zoning Officer shall issue a Land Use Permit only after it has been determined that the proposed work to be undertaken will be in conformance with the requirements of this Article and all other applicable codes and ordinances.

B. 	Prior to the issuance of any land use permit, the Zoning Officer shall review the application for the permit to determine if all other necessary government permits required by State and Federal laws have been obtained, such as those required by the Pennsylvania Sewage Facilities Act (Act 1966-537, as amended); the Pennsylvania Dam Safety and Encroachments Act (Act 1978-325, as amended); the Pennsylvania Clean Streams Act (Act 1937-394, as amended); and the U.S. Clean Water Act, Section 404, 33, U.S.C. 1344, as amended. No permit shall be issued until this determination has been made. These permits include, but are not limited to:

1. 	Permits for activities or obstructions in the floodway (as delineated on municipal Flood Insurance study maps) or within 50 feet of the top of a stream bank where no floodway is delineated. Contact the regional office of the Department of Environmental Protection for more information.

2. 	Permits for discharge of stormwater from construction activities required under the National Pollutant Discharge Elimination System Program. Contact the County Conservation District for additional information.

C. 	No encroachment, alteration, or improvement of any kind shall be made to any watercourse until all adjacent municipalities which may be affected by such action have been notified by the Township and until all required permits or approvals have been first obtained from the Department of Environmental Protection Regional Office. In addition, the Federal Emergency Management Agency and Pennsylvania Department of Community and Economic Development, shall be notified by the Township prior to any alteration or relocation of any watercourse.

Section 1503	 Application Procedures and Requirements

A. 	Application for such a building permit shall be made, in writing, to the Building Permit Officer on forms supplied by the Township. Such application shall contain the following:

1. 	Name and address of applicant.

2. 	Name and address of owner of land on which proposed construction is to occur.

3. 	Name and address of contractor.

4. 	Site location including address.

5. 	Listing of other permits required.

6. 	Brief description of proposed work and estimated cost, including a breakout of the flood-related cost and the market value of the building before the flood damage occurred.

7. 	A plan of the site showing the exact size and location of the proposed construction, as well as any existing buildings or structures.

B. 	If any proposed construction or development is located entirely or partially within any identified floodplain area, applicants for Land Use Permits shall provide all the necessary information in sufficient detail and clarity to enable the Zoning Officer to determine that:

1. 	All such proposals are consistent with the need to minimize flood damage and conform with the requirements of this and all other applicable codes and ordinances;

2. 	All utilities and facilities, such as sewer, gas, electrical and water systems are located and constructed to minimize or eliminate flood damage; and

3. 	Adequate drainage is provided so as to reduce exposure to flood hazards.

C. 	Applicants shall file the following minimum information plus any other pertinent information as may be required by the Zoning Officer to make the above determination:

1. 	A completed Land Use Permit Application Form.

2. 	A plan of the entire site, clearly and legibly drawn at a scale of one (1) inch being equal to one hundred (100) feet or less, showing the following:

a. 	North arrow, scale, and date;

b. 	Topographic contour lines, if available;

c. 	All property and lot lines including dimensions, and the size of the site expressed in acres or square feet;

d. The location of all existing and proposed buildings, structures, and other improvements, including the location of any existing or proposed subdivision and land development;

e. 	The location of all existing streets, drives, and other access ways; and

f. 	The location of any existing bodies of water or watercourses, identified floodplain areas, and, if available, information pertaining to the floodway, and the flow of water including direction and velocities.

3. 	Plans of all proposed buildings, structures and other improvements, drawn at suitable scale showing the following:

a. 	The proposed lowest floor elevation of any proposed building based upon the Vertical Datum referenced on the current municipal Flood Insurance Rate Maps;

b. 	The elevation of the one hundred (100) year flood;

c. 	If available, information concerning flood depths, pressures, velocities, impact and uplift forces and other factors associated with a one hundred (100) year flood; and

d. 	Detailed information concerning any proposed flood proofing measures.

e. 	Supplemental information as may be necessary under 34 PA Code, Chapter 401-405 as amended, and Sec.1612.5.1, Section 104.7 and 109.3 of the 2003 IBC, as amended, and Section R106.1.3 and R104.7 of the 2003 IRC, as amended.

4. 	The following data and documentation:

a. 	Documentation, certified by a registered professional engineer or architect, to show that the cumulative effect of any proposed development within an FE (Special Floodplain Area), when combined with all other existing and anticipated development, will not increase the elevation of the one hundred (100) year flood more than one (1) foot at any point.

b. 	A document, certified by a registered professional engineer or architect, which states that the proposed construction or development has been adequately designed to withstand the pressures, velocities, impact and uplift forces associated with the one hundred (100) year flood. Such statement shall include a description of the type and extent of flood proofing measures which have been incorporated into the design of the structure and/or the development.

c. 	Detailed information needed to determine compliance with the Storage, and Development Which May Endanger Human Life, including:

(1) 	The amount, location and purpose of any materials or substances referred to in this Article which are intended to be used, produced, stored or otherwise maintained on site.

(2) 	A description of the safeguards incorporated into the design of the proposed structure to prevent leaks or spills of the dangerous materials or substances listed in Section 4.04 during a one hundred (100) year flood.

d. 	The appropriate component of the Department of Environmental Protection's "Planning Module for Land Development."

e. 	Where any excavation or grading is proposed, a plan meeting the requirements of the Department of Environmental Protection, to implement and maintain erosion and sediment pollution control.

Section 1504	Review of Application by Others

A. 	A copy of all plans and applications for any proposed construction or development in any identified floodplain area to be considered for approval may be submitted by the Zoning Officer to any other appropriate agencies and/or individuals (e.g. Planning Commission, Township Engineer, etc.) for review and comment.

Section 1505	Changes

A. 	After the issuance of a building permit by the Zoning Officer, no changes of any kind shall be made to the application, permit or any of the plans, specifications or other documents submitted with the application without the written consent or approval of the Zoning Officer. Requests for any such change shall be in writing, and shall be submitted by the applicant to the Zoning Officer for consideration.

B. The Zoning Officer shall not approve changes until the applicant submits documentation that changes which may affect other state or federal permits are approved and permitted by the appropriate permitting agency.

Section 1506	Placards

A. 	In addition to the building permit, the Zoning Officer shall issue a placard which shall be displayed on the premises during the time construction is in progress. This placard shall show the number of the building permit the date of its issuance and be signed by the Zoning Officer.

Section 1507	Start of Construction

A. 	Work on the proposed construction and/or development shall begin within six (6) months and shall be completed within twelve (12) months after the date of issuance of the land use permit or the permit shall expire unless a time extension is granted, in writing, by the Zoning Officer. Construction and/or development shall be considered to have started with the preparation of land, land clearing, grading, filling, excavation of basement, footings, piers, or foundations, erection of temporary forms, the installation of piling under proposed subsurface footings, or the installation of sewer, gas and water pipes, or electrical or other service lines from the street.

B. 	Time extensions shall be granted only if a written request is submitted by the applicant, which sets forth sufficient and reasonable cause for the Zoning Officer to approve such a request.

Section 1508	Inspection and Revocation

A. 	During the construction period, the Zoning Officer or other authorized official shall inspect the premises to determine that the work is progressing in compliance with the information provided on the permit application and with all applicable municipal laws and ordinances. He shall make as many inspections during and upon completion of the work as are necessary.

B. 	In the discharge of his duties, the Zoning Officer shall have the authority to enter any building, structure, premises or development in the identified floodplain area, upon presentation of proper credentials, at any reasonable hour to enforce the provisions of this ordinance.

C. 	In the event the Zoning Officer discovers that the work does not comply with the permit application or any applicable laws and ordinances, or that there has been a false statement or misrepresentation by any applicant, the Zoning Officer shall revoke the land use permit and report such fact to the Board of Supervisors for whatever action it considers necessary.

D. 	A record of all such inspections and violations of this ordinance shall be maintained.

E. 	The requirements of the 34 PA Code Chapter 401-405 and the IBC (Sections 109.3.3 1612.5.1, 104.7 and 103.8) and the 2003 IRC (R106.1.3, 109.1.3 and R104.7) or latest revisions thereof pertaining to elevation certificates and record retention shall be considered.

Section 1509	Appeals

A. 	Any person aggrieved by any action or decision of the Zoning Officer concerning the administration of the provisions of this Article, may appeal to the Board of Supervisors. Such appeal must be filed, in writing, within thirty (30) days after the decision, determination or action of the Zoning Officer.

B. 	Upon receipt of such appeal the Board of Supervisors shall set a time and place, within not less than ten (10) or more than thirty (30) days, for the purpose of considering the appeal. Notice of the time and place at which the appeal will be considered shall be given to all parties.

C. 	Any person aggrieved by any decision of the Board of Supervisors may seek relief therefrom by appeal to court, as provided by the laws of this Commonwealth including the Pennsylvania Flood Plain Management Act, as amended.

Section 1510	Identification

The regulated floodplain areas shall consist of the following areas:

A. 	The identified floodplain areas shall be those areas of the Township, which are subject to the one hundred (100) year flood, as identified in the Flood Insurance Study (FIS) and the accompanying maps prepared for the Township by the Federal Emergency Management Agency (FEMA), the most recent revision thereof.

B. Supplemental floodplain areas which are areas not identified in the FIS but where the Township has determined the area to merit additional regulation under this Article. These areas are identified on the Township supplemental floodplain identification map. Note: Item B may be implemented by municipalities for areas not identified as floodplains on the FIS, but are determined by the municipality to merit additional regulation under this Article. These areas, if opted for should be identified on an official map.

Section 1511	Description of Floodplain Areas

The identified floodplain area shall consist of the following specific areas:

A. 	FW (Floodway Area) - the areas identified as "Floodway" in the AE Zone in the Flood Insurance Study prepared by the FEMA. The term shall also include floodway areas which have been identified in other available studies or sources of information for those floodplain areas where no floodway has been identified in the Flood Insurance Study.

B. 	FF (Flood-Fringe Area) - the remaining portions of the one hundred (100) year floodplain in those areas identified as an AE Zone in the Flood Insurance study, where a floodway has been delineated. The basis for the outermost boundary of this area shall be the one hundred (100) year flood elevations as shown in the flood profiles contained in the Flood Insurance Study.

Note: It is possible that the following provisions pertaining to an FE area may not be needed. In some instances a Flood Insurance Study will be prepared which will not include this kind of floodplain area, in which case the following provisions should be deleted, as well as all references to an FE area.

C. 	FE (Special Floodplain Area) - the areas identified as Zone AE in the Flood Insurance Study, where one hundred (100) year flood elevations have been provided, but no floodway has been delineated.

D. FA (General Floodplain Area) - the areas identified as Zone A in the FIS for which no one hundred (100) year flood elevations have been provided. When available, information from other Federal, State, and other acceptable sources shall be used to determine the one hundred (100) year elevation, as well as a floodway area, if possible. When no other information is available, the one hundred (100) year elevation shall be determined by using a point on the boundary of the identified floodplain area which is nearest the construction site in question. In lieu of the above, the Township may require the applicant to determine the elevation with hydrologic and hydraulic engineering techniques. Hydrologic and hydraulic analyses shall be undertaken only by professional engineers or others of demonstrated qualifications, who shall certify that the technical methods used correctly reflect currently accepted technical concepts. Studies, analyses, computations, etc., shall be submitted in sufficient detail to allow a thorough technical review by the Township.

E. 	SA (Supplemental Floodplain Area) – Areas not identified in the FIS but where the Township has determined the area to merit additional regulation under this Article.

Section 1512	Changes in Identification of Area

The identified floodplain area as shown on the FIS maps may be revised or modified by the Board of Supervisors where studies or information provided by a qualified agency or person documents the need for such revision. However, prior to any such change, approval must be obtained from the Federal Emergency Management Agency (FEMA).

Section 1513	Boundary Disputes

Should a dispute concerning any identified floodplain boundary arise, an initial determination shall be made by the Township Planning Commission and any party aggrieved by this decision or determination may appeal to the Board of Supervisors. The burden of proof shall be on the appellant.

Section 1514	General

A. 	No encroachment, alteration, or improvement of any kind shall be made to any watercourse until all adjacent municipalities which may be affected by such action have been notified by the Township, and until all required permits or approvals have been first obtained from the Department of Environmental Protection Regional Office. In addition, the Federal Emergency Management Agency and Pennsylvania Department of Community and Economic Development, shall be notified prior to any alteration or relocation of any watercourse.

B. 	Any new construction, development, uses or activities allowed within any identified floodplain area, shall be undertaken in strict compliance with the provisions contained in this Article and any other applicable codes, ordinances and regulations.

Section 1515	Special Requirements for FW, FF, FE and FA and SA Areas

A. Within any identified floodplain area new construction or development is prohibited with the following exceptions provided the use does not require structures other than as indicated or fill other than as indicated:

1. 	Accessory uses such as sheds or pavilions. Such uses are limited to 600 square feet of floor area. The total amount of floor area per lot for accessory uses is limited to 600 square feet regardless of the number of such accessory structures.

2. 	Plowing, seeding, harvesting, pasture plant nurseries, horticulture, forestry, aquaculture and other normal farming operations.

3. 	Vehicle access uses including driveways, roads, streets, bridges and culverts. Impacts to the floodplain are limited to the least amount needed to construct the use and provide safety and structural integrity.

4. 	Public and Private recreational uses such as parks, camps, picnic areas, swimming areas, boat launches, wildlife areas and preserves, hunting and fishing, game farms, trails for hiking, horse riding, athletic fields and other recreational activities.

5. 	Accessory residential uses such as yards, gardens and play areas.

6. 	Projects conducted with the objective of improvement, stabilization, restoration, or enhancement of the stream bank, stream channel, floodplain, watershed hydrology, riparian buffers or aquatic habitat, and maintenance activities associated with such projects. These projects include but are not limited to agricultural and stormwater management best management practices. Such projects must receive appropriate permits and approvals from DEP prior to starting the project.

7. 	Utility lines and pipes.

8. 	Similar uses determined to be acceptable by the Board of Supervisors provided the use does not require structures other than as indicated above or fill other than as indicated above.

B. 	Pre-Existing lots or parcels:

1. 	Where a lot or parcel that has been legally created and recorded prior to the effective date of this Article is located entirely or partially within any identified floodplain area, the following conditions apply:

a. 	If the lot or parcel is located entirely within any identified floodplain area, development may be allowed by special exception. Such development shall be in full compliance with all other requirements of this Article.

b. 	If the lot or parcel is located partially within any identified floodplain area, development shall be confined to the area outside of the floodplain area to the maximum extent practical. If the area outside of the floodplain area is insufficient for the proposed use, development within the floodplain may be allowed by a variance. Such development shall be in full compliance with all other requirements of this ordinance.

C. 	Creation of new lots or parcels

1. 	Any new lots or parcels created after the effective date of this Article shall contain adequate area outside of any identified floodplain for the proposed use.

D. 	With any FW (Floodway Area), the following provisions apply:

1. 	Any new construction, development, use, activity, or encroachment allowable under this Article that would cause any increase in flood heights shall be prohibited.

2. 	No new construction or development shall be allowed, unless a permit is obtained from the Department of Environmental Protection Regional Office.

E. 	Within any FE (Special Floodplain Area), new construction or development allowable under this Article shall not be permitted unless it is demonstrated that the cumulative effect of the proposed development, when combined with all other existing and anticipated development, will not increase the elevation of the one hundred (100) year flood more than one (1) foot at any point.

F. 	Within any FE (Special Floodplain Area), FF (Flood-Fringe Area), FA (General Floodplain Area) or SA (Supplemental Floodplain Area), the following provisions apply:

1. 	No new construction or development allowable under this ordinance shall be located within the area measured fifty (50) feet landward from the top-of-bank of any watercourse, unless a permit is obtained from the Department of Environmental Protection Regional Office.

2. 	All allowable uses shall be conducted in full compliance with this Article.

G. Within any identified floodplain area and within 50 feet of the top of bank of any stream not located within an identified floodplain area, the following uses are expressly prohibited:

1. 	Development Which May Endanger Human Life

a. 	Any new or substantially improved structures, or expansion or enlargement of any structure which:

(1) Will be used for the production or storage of any of the following dangerous materials or substances; or,

(2) 	Will be used for any activity requiring the maintenance of a supply of any amount of any of the following dangerous materials or substances on the premises; or,

(3) 	Will involve the production, storage, or use of any amount of radioactive substances;

b. 	The following list of materials and substances are considered dangerous to human life:

Acetone

Ammonia

Benzene

Calcium carbide

Carbon disulfide

Celluloid

Chlorine

Hydrochloric acid

Hydrocyanic acid

Magnesium

Nitric acid and oxides of nitrogen

Petroleum products (gasoline, fuel oil, etc.)

Phosphorus

Potassium

Sodium

Sulphur and Sulphur products

Pesticides (including herbicides, insecticides, fungicides, and rodenticides)

Radioactive substances, insofar as such substances are not otherwise regulated.

c. 	The above prohibition does not apply to normal amounts of any product composed of the above materials maintained for residential use. Such uses include but are not limited to the following:

(1) Normal amounts of petroleum based home heating oil or petroleum based fuels maintained for residential use.

(2) 	Normal amounts of cleaning product composed of the above materials maintained for residential use.

(3) Normal amounts of pesticides (including herbicides, insecticides fungicides, and rodenticides) maintained for residential use.

2. 	Special Permit Activities - The commencement of any of the following activities; or the construction, enlargement, or expansion of any structure used, or intended to be used, for any of the following activities:

a. 	Hospitals

b. 	Nursing homes

c. 	Jails or prisons

3. 	Manufactured homes, manufactured home parks, expansion of existing manufactured home parks.

Section 1516	Elevation and Floodproofing Requirements

A. 	Residential Structures

1. 	Within any identified floodplain area, any new construction or substantial improvement of a residential structure shall have the lowest floor (including basement) elevated to a minimum of 1.5 feet above the regulatory flood elevation. The design and construction standards and specifications contained in the 2003 IBC, as amended, (Sec. 1612.4,1603.1.6 and 3403.1) and in the 2003 IRC, as amended, (Sec. R323.1.4, R323.2.1, and R323.2.2) and ASCE 24 (Sec. 2.4 and 2.5, Chap. 5 as amended) and 34 PA Code (Chapters 401-405 as amended) shall be utilized.

B. 	Non-Residential Structures

1. 	Within any identified floodplain area, any new construction or substantial improvement of a nonresidential structure shall have the lowest floor (including basement) elevated to a minimum of 1.5 feet above the regulatory flood elevation, or be designed and constructed so that the space enclosed by such structure shall remain either completely or essentially dry during any flood up to that height. Such floodproofing shall be in compliance with the WI or W2 space classification standards contained in the publication entitled "Flood-Proofing Regulations" published by the U.S. Army Corps of Engineers (June 1972, as amended) or with some other equivalent standard. All plans and specifications for such floodproofing shall be accompanied by a statement certified by a registered professional engineer or architect which states that the proposed design and methods of construction are in conformance with the above referenced standards.

2. 	The design and construction standards and specifications contained in the IBC (Sec. 1603.1.2, 1603.1.6, 1605.2.2, 1606.5, 1612.5.1 and 3403.1. as amended) and ASCE 24 (Secs. 2.4 and Chap. 7 as amended) and 34 PA Code (Chapters 401-405 as amended) shall be utilized.

C. 	Space below the lowest floor.

1. 	Fully enclosed space below the lowest floor (including basement) is prohibited.

2. 	Partially enclosed space below the lowest floor (including basement) which will be used solely for the parking of a vehicle, building access, or incidental storage in an area other than a basement, shall be designed and constructed to allow for the automatic entry and exit of flood waters for the purpose of equalizing hydrostatic forces on exterior walls. The term "partially enclosed space" includes crawl spaces. Designs for meeting this requirement must either be certified by a registered professional engineer or architect, or meet or exceed the following minimum criteria:

a. 	A minimum of two openings having a net total area of not less than one (1) square inch for every square foot of enclosed space.

b. 	The bottom of all openings shall be no higher than one (1) foot above grade.

c. 	Openings may be equipped with screens, louvers, etc. or other coverings or devices provided that they permit the automatic entry and exit of floodwaters.

3. 	Consideration may be given to the requirements of 34 PA Code (Chapters 401-405 as amended) and the 2003 IRC (Secs.R323.2.2 and R323.1.4 as amended) and the 2003 IBC (Secs. 1612.4, 1612.5, 1202.3.2 and 1203.3.3. as amended).

D. 	Accessory structures – accessory structures allowable under this Article need not be elevated or requirements:

1. 	The structure shall not be designed or used for human habitation, but shall be limited to the parking of vehicles, or to the storage of tools, material, and equipment related to the principal use or activity.

2. 	Floor area shall not exceed 600 square feet. The total amount of floor area per lot for accessory uses is limited to 600 square feet regardless of the number of such accessory structures.

3. 	The structure will have a low damage potential.

4. 	The structure will be located on the site so as to cause the least obstruction to the flow of flood waters.

5. 	Power lines, wiring, and outlets will be at least one and one-half (1 ½) feet above the 100 year flood elevation.

6. 	Permanently affixed utility equipment and appliances such as furnaces, heaters, washers, dryers, etc. are prohibited.

7. 	Sanitary facilities are prohibited.

8. 	The structure shall be adequately anchored to prevent flotation or movement and shall be designed to automatically provide for the entry and exit of floodwater for the purpose of equalizing hydrostatic forces on the walls. Designs for meeting this requirement must either be certified by a registered professional engineer or architect, or meet or exceed the following minimum criteria:

a. 	A minimum of two openings having a net total area of not less than one (1) square inch for every square foot of enclosed space.

b. 	The bottom of all openings shall be no higher than one (1) foot above grade.

c. 	Openings may be equipped with screens, louvers, etc. or other coverings or devices provided that they permit the automatic entry and exit of flood waters.

Section 1517	Design and Construction Standards

The following minimum standards shall apply for all construction and development allowable under this Article proposed within any identified floodplain area:

A. 	If fill is used, it shall:

1. 	extend laterally at least fifteen (15) feet beyond the building line from all points;

2. 	consist of uncontaminated soil or small rock materials only;

3. 	be compacted to provide the necessary permeability and resistance to erosion, scouring, or settling;

4. 	be no steeper than one (1) vertical to two (2) horizontal, feet unless substantiated data, justifying steeper slopes are submitted to, and approved by the Zoning Officer;

5. 	be used to the extent to which it does not adversely affect adjacent properties. The provisions contained in the 2003 IBC (Sec. 1801.1 and 1803.4) shall be utilized.;

6. 	be limited to only the amount needed for the intended use;

7. 	Sanitary Landfills shall not be permitted;

B. 	Drainage Facilities.  Storm drainage facilities shall be designed to convey the flow of storm water runoff in a safe and efficient manner. The system shall insure proper drainage along streets, and provide positive drainage away from buildings. The system shall also be designed to prevent the discharge of excess runoff onto adjacent properties. The provisions contained in the 2003 IBC (Appendix G401.5 as amended) shall be utilized.

C. 	Water and Sanitary Sewer Facilities and Systems

1. 	All new or replacement water and sanitary sewer facilities and systems shall be located, designed and constructed to minimize or eliminate flood damages and the infiltration of flood waters.

2. 	Sanitary sewer facilities and systems shall be designed to prevent the discharge of untreated sewage into flood waters.

3. 	No part of any on-site sewage system shall be located within any identified floodplain area except in strict compliance with all State and local regulations for such systems. If any such system is permitted, it shall be located so as to avoid impairment to it, or contamination from it, during a flood.

4. 	The design and construction provisions of the UCC, Uniform Construction Code, as amended, and 34 PA Code (Chapters 401-405 as amended) and contained in the 2003 IBC (Appendix G. Secs. 401.3 and 401.4 as amended), the 2003 IRC (Sec. 323.1.6 as amended), the ASCE 24-98 (Sec. 8.3 as amended), FEMA, #348 as amended, “Protecting Building Utilities From Flood Damages” and The International Private Sewage Disposal Code (Chapter 3 as amended) shall be utilized.

D. 	Other Utilities

1. 	All other utilities such as gas lines, electrical and telephone systems shall be located, elevated (where possible) and constructed to minimize the chance of impairment during a flood.

E. 	Streets

1. 	The finished elevation of all new streets shall be no more than one (1) foot below the Regulatory Flood Elevation.

F. 	Storage

1. 	All materials that are buoyant, flammable, and explosive or, in times of flooding, could be injurious to human, animal, or plant life, and not listed in this article under Development Which May Endanger Human Life, shall be stored at or above the Regulatory Flood Elevation and/or flood proofed to the maximum extent possible.

G. 	Placement of Buildings and Structures

1. 	All buildings and structures allowable under this Article shall be designed, located, and constructed so as to offer the minimum obstruction to the flow of water and shall be designed to have a minimum effect upon the flow and height of flood water.

H. 	Anchoring

1. All buildings and structures shall be firmly anchored in accordance with accepted engineering practices to prevent flotation, collapse, or lateral movement.

2. All air ducts, large pipes, storage tanks, and other similar objects or components located below the Regulatory Flood Elevation shall be securely anchored or affixed to prevent flotation.

3. The design and construction requirements of the UCC pertaining to this subsection as referred to in 34 PA Code (Chapters 401-405 as amended) and contained in the 2003 IBC (Secs. 1605.2.2, 1605.3.1.2, 1612.4 and Appendix G501.3 as amended), the IRC (Secs. R301.1 & R323.1.1 as amended) and ASCE 24-98 (Sec. 5.6 as amended) shall be utilized.

I. 	Floors, Walls and Ceilings

1. 	Wood flooring used at or below the Regulatory Flood Elevation shall be installed to accommodate a lateral expansion of the flooring, perpendicular to the flooring grain without causing structural damage to the building.

2. 	Plywood used at or below the Regulatory Flood Elevation shall be of a "marine” or "water-resistant" variety.

3. 	Walls and ceilings at or below the Regulatory Flood Elevation shall be designed and constructed of materials that are "water-resistant" and will withstand inundation.

4. 	Windows, doors, and other components at or below the Regulatory Flood Elevation shall be made of metal or other "water-resistant" material.

5. 	The provisions of the UCC pertaining to this subsection and referenced in the 34 PA Code (Chapters 401-405 as amended) and contained in the 2003 IBC (Secs. 801.1.3, 1403.2, 1403.4, 1403.6 and 1404.2 as amended), the 2003 IRC (Secs. R323.1.7 & R501.3 as amended) and ASCE 24-98 (Chapter 6 as amended) shall be utilized.

J. 	Paints and Adhesives

1. 	Paints and other finishes used at or below the Regulatory Flood Elevation shall be of "marine" or "water-resistant" quality.

2. 	Adhesives used at or below the Regulatory Flood Elevation shall be of a "marine" or "water-resistant" variety.

3. 	All wooden components (doors, trim, cabinets, etc.) shall be finished with a "marine" or "water-resistant" paint or other finishing material. The standards and specifications contained in 34 PA Code (Chapters 401-405, amended) the 2003 IBC (Secs. 801.1.3, 1403.7 and Appendix G as amended) and the 2003 IRC (Secs. R323.1.7 as amended) shall be utilized.

K. 	Electrical Components

1. 	Electrical distribution panels shall be at least three (3) feet above the one hundred (100) year flood elevation.

2. 	Separate electrical circuits shall serve lower levels and shall be dropped from above.

3. 	The provisions pertaining to the above provisions and referenced in the UCC as amended and 34 PA Code (Chapters 401-405) as amended and contained in the 2003 IBC (Sec. 1612.4 as amended), the IRC (Sec. R323.1.5 as amended), the 2000 IFGC (Secs. R301.5 and R1601.3.8 as amended) and ASCE 24 (Chapter 8 as amended) shall be utilized.

L. 	Equipment

1. 	Water heaters, furnaces, air conditioning and ventilating units, and other electrical, mechanical or utility equipment or apparatus shall not be located below the Regulatory Flood Elevation.

2. 	The provisions pertaining to the above provision and referenced in the UCC as amended and 34 PA Code (Chapters 401-405), as amended and contained in the 2003 IBC (Sec. 1612.4 as amended), the 2003 IRC (Secs. R323.1.5 as amended) the 2000 IFGC (Secs. R301.5 and R1601.3.8 as amended) and ASCE 24 (Chapter 8 as amended) shall be utilized.

M. 	Fuel Supply Systems

1. 	All gas and oil supply systems shall be designed to prevent the infiltration of flood waters into the system and discharges from the system into flood waters. Additional provisions shall be made for the drainage of these systems in the event that flood water infiltration occurs.

Section 1518	Uniform Construction Code Coordination

A. 	The Standards and Specifications contained 34 PA Code (Chapters 401-405), as amended and not limited to the following provisions shall apply to the above and other sections and sub-sections of this Article, to the extent that they are more restrictive and/or supplement the requirements of this Article.

1. 	International Building Code (IBC) 2003 or the latest edition thereof: Secs. 801, 1202, 1403, 1603, 1605, 1612, 3402, and Appendix G.

2. 	International Residential Building Code (IRC) 2003 or the latest edition thereof: Secs R104, R105, R109, R323, Appendix AE101, Appendix E and Appendix J.

Section 1519	Existing Structures

A. 	The provisions of this Article do not require any changes or improvements to be made to lawfully existing structures. However, when an improvement is made to any existing structure, the provisions of the underlying zoning district shall apply.

Section 1520	Improvements

A. 	The following provisions shall apply whenever any improvement is made to an existing structure located within any identified floodplain area:

1. 	No expansion or enlargement of an existing structure shall be allowed within any floodway area that would cause any increase in the elevation of the one hundred (100) year flood.

2. 	No expansion or enlargement of an existing structure shall be allowed within any FE area that would, together with all other existing and anticipated development, increase the one hundred (100) year flood elevation more than one (1) foot at any point.

3. 	Any modification, alteration, reconstruction, or improvement, of any kind to an existing structure, to an extent or amount of fifty (50) percent or more of its market value, shall constitute a substantial improvement and shall be undertaken only in full compliance with the provisions of this Article. NOTE: The above activity shall also address the requirements of the 34 PA Code Chapters 401-405, as amended and the 2003 IBC (Sec. 3402.1 and 1612.4 as amended) and the 2003 IRC (Secs. R105.3.1.1 and 323.1.4 as amended).

4. 	Any modification, alteration, reconstruction, or improvement of any kind to an existing structure, to an extent or amount of less than fifty (50) percent of its market value, shall be elevated and/or floodproofed to the greatest extent possible.

5. 	Any modification, alteration, reconstruction, or improvement of any kind that meets the definition of “repetitive loss” shall be undertaken only in full compliance with the provisions of this ordinance

6. 	The requirements of 34 PA Code Chapter 401-405, as amended and the 2003 IRC (Secs. R102.7.1, R105.3.1, R105.3.1.1 and Appendices E and J) or the latest revision thereof and the 2003 IBC (Secs. 101.3, 3403.1 and Appendix G) or the latest revision thereof shall also be utilized in conjunction with the provisions of this section.

Section 1521	Definitions

The following words are defined in order to facilitate the interpretation of this Article for administrative purposes and in the carrying out of duties by appropriate officers and by the Zoning Hearing Board.  Unless otherwise expressly stated, the following words shall, for the purposes of this Article, have the meaning herein indicated.

A. 	Accessory use or structure - a use or structure on the same lot with, and of a nature customarily incidental and subordinate to, the principal use or structure.

B. 	Basement - A space having one-half or more of its floor-to-ceiling height above the average level of the adjoining ground and with a floor-to-ceiling height of not less than six and a half feet.

C. 	Building - a combination of materials to form a permanent structure having walls and a roof. Included shall be all manufactured homes and trailers to be used for human habitation.

D. 	Completely dry space - a space which will remain totally dry during flooding; the structure is designed and constructed to prevent the passage of water and water vapor.

E. 	Development - any man-made change to improved or unimproved real estate, including but not limited to the construction, reconstruction, renovation, repair, expansion, or alteration of buildings or other structures; the placement of manufactured homes; streets, and other paving; utilities; filling, grading and excavation; mining; dredging; drilling operations; storage of equipment or materials; and the subdivision of land.

F. 	Essentially dry space - a space which will remain dry during flooding, except for the passage of some water vapor or minor seepage; the structure is substantially impermeable to the passage of water.

G. 	Flood - a temporary inundation of normally dry land areas.

H. 	Floodplain area - a relatively flat or low land area which is subject to partial or complete inundation from an adjoining or nearby stream, river or watercourse; and/or any area subject to the unusual and rapid accumulation of surface waters from any source.

I. 	Floodproofing - means any combination of structural and nonstructural additions, changes, or adjustments to structures which reduce or eliminate flood damage to real estate or improved real property, water and sanitary facilities, structures and their contents.

J. 	Floodway - the designated area of a floodplain required to carry and discharge flood waters of a given magnitude. For the purposes of this Article, the floodway shall be capable of accommodating a flood of the one hundred (100) year magnitude.

K. 	Historic structure - any structure that is:

1. 	Listed individually in the National Register of Historic Places (a listing maintained by the Department of Interior) or preliminarily determined by the Secretary of the Interior as meeting the requirements for individual listing on the National Register;

2. 	Certified or preliminarily determined by the Secretary of the Interior as contributing to the historical significance of a registered historic district or a district preliminarily determined by the Secretary to qualify as a registered historic district;

3. 	Individually listed on a state inventory of historic places in states with historic preservation programs which have been approved by the Secretary of Interior; or

4. 	Individually listed on a local inventory of historic places in communities with historic preservation programs that have been certified either:

a) 	By an approved state program as determined by the Secretary of the Interior or

b) 	Directly by the Secretary of the Interior in states without approved programs.

L. 	Identified floodplain area - the floodplain area specifically identified in this Article as being inundated by the one hundred (100) year flood.

M. 	Land development - Any of the following activities:

1. 	The improvement of one lot or two or more contiguous lots, tracts, or parcels of land for any purpose involving:

a. 	a group of two or more residential or nonresidential buildings, whether proposed initially or cumulatively, or a single nonresidential building on a lot or lots regardless of the number of occupants or tenure; or

b. 	the division or allocation of land or space, whether initially or cumulatively, between or among two or more existing or prospective occupants by means of, or for the purpose of streets, common areas, leaseholds, condominiums, building groups or other features.

c. 	A subdivision of land.

N. 	Lowest floor - the lowest floor of the lowest fully enclosed area (including basement). An unfinished, flood resistant partially enclosed area, used solely for parking of vehicles, building access, and incidental storage, in an area other than a basement area is not considered the lowest floor of a building, provided that such space is not designed and built so that the structure is in violation of the applicable non-elevation design requirements of this Article.

O. 	Manufactured home - a structure, transportable in one or more sections, which is built on a permanent chassis, and is designed for use with or without a permanent foundation when attached to the required utilities. The term includes park trailers, travel trailers, recreational and other similar vehicles which are placed on a site for more than 180 consecutive days.

P. 	Manufactured home park - a parcel of land under single ownership, which has been planned and improved for the placement of two or more manufactured homes for non-transient use.

Q. 	Minor repair - the replacement of existing work with equivalent materials for the purpose of its routine maintenance and upkeep, but not including the cutting away of any wall, partition or portion thereof, the removal or cutting of any structural beam or bearing support, or the removal or change of any required means of egress, or rearrangement of parts of a structure affecting the exit way requirements; nor shall minor repairs include addition to, alteration of, replacement or relocation of any standpipe, water supply, sewer, drainage, drain leader, gas, oil, waste, vent, or similar piping, electric wiring or mechanical or other work affecting public health or general safety.

R. 	New construction - structures for which the start of construction commenced on or after the adoption of this Ordinance , and includes any subsequent improvements thereto.

S. 	One hundred year flood - a flood that, on the average, is likely to occur once every one hundred (100) years (i.e. that has one (1) percent chance of occurring each year, although the flood may occur in any year).

T. 	Person - A corporation, company, association, society, firm, partnership, or joint stock company, as well as an individual, a state, and all political subdivisions of a state or any agency or instrumentality thereof, or any other legal entity whatsoever, which is recognized by law as the subject of rights and duties.

U. 	Recreational vehicle - a vehicle which is (i) built on a single chassis; (ii) not more than 400 square feet, measured at the largest horizontal projections; (iii) designed to be self-propelled or permanently towable by a light-duty truck; (iv) not designed for use as a permanent dwelling but as temporary living quarters for recreational, camping, travel, or seasonal use.

V. 	Regulatory flood elevation - the one hundred (100) year flood elevation plus a freeboard safety factor of one and one-half (1½) feet.

W. Repetitive loss – flood related damages sustained by a structure on two separate occasions during a 10-year period for which the cost of repairs at the time of each such flood event, on average, equals or exceeds 25 percent of the market value of the structure before the damages occurred.

X. 	Structure – Any man-made object having an ascertainable stationary location on or in land or water, whether or not affixed to the land.

Y. 	Subdivision - the division or redivision of a lot, tract, or parcel of land by any means into two or more lots, tracts, parcels or other divisions of land including changes in existing lot lines for the purpose, whether immediate or future, of lease, partition by the court for distribution to heirs, or devisees, transfer of ownership or building or lot development: Provided, however, that the subdivision by lease of land for agricultural purposes into parcels of more than ten acres, not involving any new street or easement of access or any residential dwelling, shall be exempted.

Z. Substantial additions to manufactured home parks – Any repair, reconstruction, or improvement of an existing manufactured home park or manufactured home subdivision, where such repair, reconstruction, or improvement of the streets, utilities, and pads will equal or exceed 50% of the value of the streets , utilities, and pads before the repair, reconstruction, or improvement is started.

AA.	Substantial damage - damage from any cause sustained by a structure whereby the cost of restoring the structure to its before-damaged condition would equal or exceed fifty (50) percent or more of the market value of the structure before the damage occurred.

BB. 	Substantial improvement - Any reconstruction, rehabilitation, addition, or other improvement of a structure, the cost of which equals or exceeds fifty (50) percent of the market value of the structure before the "start of construction" of the improvement. This term includes structures which have incurred "substantial damage (or “repetitive loss” when a repetitive loss provision is used) regardless of the actual repair work performed. The term does not, however include either:

1. 	Any project for improvement of a structure to correct existing violations of state or local health, sanitary, or safety code specifications which have been identified by the local code enforcement official and which are the minimum necessary to assure safe living conditions, or;

2. 	Any alteration of a “historic structure,” provided that the alteration will not preclude the structure's continued designation as a "historic structure.”

CC. Uniform Construction Code (UCC) – The statewide building code adopted by The Pennsylvania General Assembly in 1999, and as amended, applicable to new construction in all municipalities whether administered by the municipality, a third party or the Department of Labor and Industry. Applicable to residential and commercial buildings, The Code adopted The International Residential Code (IRC) and the International Building Code (IBC), by reference, as the construction standard applicable with the Commonwealth floodplain construction. For coordination purposes, references to the above are made specifically to various sections of the IRC and the IBC.